## Slide 1: Project Presentation
SIST_SI100B_RoboWriter
丁宁 姜泊含 马睿奕 Group ID：2

## Slide 2
Code Structure
Character_maker: A contour generation tool based on OpenCV and Bezier curves ,whcan store the contours of the given characters in the "character_contours" folder with the form of grid coordinates
Character_contours: A folder containing the coordinates of the grid points, which can be read by “mujoco_painter”
mujoco_painter: This part can import the coordinates into the mujoco program and subjected to linear fitting and IK calculations, so as to visualize and output the string.

## Slide 3
Core Code Analysis:character_maker
Draw the characters in the center and with high contrast on the blank canvas, which is convenient for subsequent opencv to recognize the contours.
1. Check boundary conditions
2. Calculate cumulative distances(Euclid distance)
3. Compute equidistant step size
4. Interpolate to generate new points

## Slide 4
Core Code Analysis:character_maker
extract_contour_points:Use OpenCV to extract character outlines(core function)
image binaryzation:Divide the image into black and white, enhance the contrast, and make it easier for OpenCV to recognize.
contour extraction:Keep all the points of the contour, and normalize them to facilitate the subsequent limitation of the character coordinates within the working range of the ur5e robotic arm.
#Perform canny edge detection to extract contours in partially connected characters
Evenly distribute the points:Remove the noise points and obtain the final coordinates.
Final result:After sampling each contour separately and assigning point numbers, the resulting coordinate point array is combined, which constitutes the coordinate point array of the overall contour of the character.

## Slide 5
Core Code Analysis:character_maker
Scale the already normalized coordinate grid proportionally to the operating range of the ur5e (default:0.2 - 0.6)
Save the coordinate data in txt format in the "Character_contours" folder.

## Slide 6
Visualize the coordinate point grid to make debugging easier
Core Code Analysis:character_maker
Omit the subsequent procedures……
←Effect demonstration

## Slide 7
Core Code Analysis:mujoco_painter
----The main structure of this program and the part of IK calculation refer to the sample program provided in class.
#Control the movement of lifting and lowering the pen to avoid the connection of strokes.
#Read the coordinates from the data file

## Slide 8
Core Code Analysis:mujoco_painter
Perform another Bezier interpolation to ensure smooth output of the Mujoco robotic arm.
During actual testing, if this step is not carried out, the robotic arm would twitch due to frequent discrete point jumps.

## Slide 9
Core Code Analysis:mujoco_painter
Add the pen-up and pen-down mechanism: In previous tests, we found that the previous Bezier function would connect strokes that were not supposed to be connected. Therefore, we added a pen-up and pen-down judgment mechanism: when the distance between the two initial coordinate points is greater than a certain value, it is identified as a pen-up point and no interpolation processing is performed.
→Non-discontinuity point, normal interpolation
→Discontinuity point, skip

## Slide 10
Core Code Analysis:mujoco_painter
Generate a smooth curve to facilitate the drawing by mujoco.
Generate handwriting only when the pen is lifted.

## Slide 11
Core Code Analysis:mujoco_painter
In the IK section of the code, we initially attempted to apply the IK solver from lec3, but encountered a problem of singular value oscillation:
We adopted two solutions:
1.Reduce the initial side length of the simulated cube
2.Set a simulation accuracy level, so that the program stops the simulation once it reaches that accuracy level.
After the test, the twitching problem was significantly improved. However, during the point-by-point simulation, even minor disturbances could cause variations in the final character shape. Therefore, we ultimately abandoned this IK solution method based on the simulation of random cube vertices and instead used the IK solver provided by Mujoco.

## Slide 12
Core Code Analysis:muti-charaters
The previous two programs could handle any single character, but were limited in handling multiple characters. Therefore, we retained the original algorithm and integrated the two programs into a new program that can handle multiple characters as well as reproduce them in mujoco.
While ensuring that the robotic arm does not experience any jerking, by adjusting the target range of coordinate scaling, the function of being able to write multiple characters simultaneously was achieved.

## Slide 13
Core Code Analysis:muti-curve-charaters
Based on the multi-character method, all that is needed is to add the relevant operations of three-dimensional Euclid distance with calculation related to spatial vectors, the goal of spherical writing can be achieved.

## Slide 14
Result
Character_contours
The content of the coordinate data txt file

## Slide 15
Result
(character_maker)Input: 1 飞 0.2 0.6

## Slide 17
Result
(mujoco_painter)Input: {coordinate file}
Final Result

## Slide 18
Result
(muti-character)Input:
No choice needed. Click to continue.

## Slide 19
Result

## Slide 20
Result
(muti-curve-character)Input:
No choice needed. Click to continue.

## Slide 21
Result

## Slide 22
Test Sample 1: Rare Characters
Original input:瓍
analysis：The overall structure of the font has been replicated, but due to the excessive number of strokes, there are still some parts that are stuck together.
Test Sample 2: Common Characters
Original input:人
analysis：A nearly perfect reproduction
Test Sample 3: Special symbols
Original input:@
analysis：There is still a slight adhesion, but it can be restored to the correct shape.
Some test samples

## Slide 23
Test Sample 4: English
Original input:ABC
analysis：The adjacent parts of the letters are stuck together, which also indicates the limitations of mujoco_painter in handling multiple characters.
Test Sample 5: (muti-character)
Original input:ABC
analysis：There is no adhesion between the letters, and there are no incorrect connections within the letters either.
Test Sample 6: (muti-character)
Original input:姜 泊 含
analysis：All three characters can be output normally, and there is no sticking or overlapping between or within the characters.

## Slide 24
Test Sample 7: Curve Characters（three-characters)
Original input:姜泊含
analysis：It can demonstrate the curvature effect, but when writing the last character, due to the setting of calculation time, there is a phenomenon of stroke loss.
Test Sample 8: Curve Characters（two-characters)
Original input:姜泊
analysis：It has very well matched the curvature of the surface and completed the output.

## Slide 25
Reflection and Anticipation
limitations:
1.Due to the fundamental principles of the algorithm, it is still impossible to completely avoid the problem of stroke connection. If different parts of a character are close to each other, the Bezier fitting in the mujoco part will incorrectly connect these different parts, resulting in stroke connection. This is more obvious in some complex characters and special characters.
2.When dealing with multi-character processing (especially when characters are separated by spaces), if the horizontal length of the string is too long, it may not be fully recognized or may be misidentified, resulting in the characters becoming elongated or partially missing.
3.When writing on a curved surface, the character shapes may change due to the deviation in the calculation of the three-dimensional Euclid distance.
The fitting effect of the curved surface writing is not very satisfactory and further improvements are needed.

## Slide 26
Reflection and Anticipation
potential improvements:
1.Further improve the character scanning logic to adapt to multi-character writing
or lengthen the range of width to contain more characters.
2.Further practice and adjustment of the applicable conditions for Bezier fitting in mujoco_painter are carried out. When the distance between two interpolation points is greater than a certain specific value, the fitting will no longer be performed to avoid incorrect connection of different parts of the character.
3.Improve the function of the curved surface writing section,extend the calculation time and add a three-dimensional vector algorithm for surface calculation.
4.Change the way of searching for characters in multi-character mode (the original method was to bind ASCII codes, which might ignore some special characters), and make it directly outline the contours using OpenCV.

## Slide 27
Work allocation
Ding Ning:
Compatibility of the two main programs (enabling the mujoco_painter to read data files) and standardized expression;
Analysis of the understanding of the reference programs presented in class;
The manager of the Github repository, the person in charge of data collection and bonus submission
Jiang Bohan:
Programming of the character_maker program;
Implementation of bonus features for surface writing and multi-character writing sections;
Learned OpenCV and applied it to the project, ensuring that the program can handle rare characters and special symbols properly.
Ma Ruiyi:
The writing of the mujoco_painter part;
The design of coordinate normalization in the character_maker program;
The overall construction of the program's thinking process;
The writer of this presentation and report.

## Slide 28: Thank you for your attention